# Duffy Lab Beamtime Checklist

## Basics

- DACs

  - Are the set screws up?

  - Open cell for security screening

- Lab notebook, with information for each DAC:

  - Diamond numbers, thicknesses, culet sizes

  - Seat types

  - Samples

  - Experimental plan

- Lab laptop

- Portable hard drive

- Relevant literature

- JCPDS cards for all expected phases

- National lab badges

  - All experimenters cleared?

  - 1st time experimenters/expired badges notified badge office?

  - All experimenters’ training up to date?

## Sample preparation

- Unloaded DACs

  - Check alignment

  - Prepare gaskets

  - Clean

- DACs 1, 2 (for making sample foils)

- Extra sample material

  - Pre-ground, mixed sample powders

  - Polished single crystals

  - Pt/Au/other pressure standard/laser absorber

  - NaCl/other media

  - Rubies (pack small portion, leave most in lab)

  - Pre-dried in furnace for >few hrs?

- Prepared gaskets

- Spare gaskets

  - Re

  - Steel

  - X-ray transparent (Be, B, cBN, etc.)?

- Gasket supports

- Spacer

- Clay/wax

  - Sculpey

  - Sticky-tak (easily removed from Be gaskets)

- Spare Belleville washers

- Hex keys

  - 10-32x1

  - 10-32x1/4 (T key for set screws)

  - 3-48 (tiny set screws)

- Spare 3-48 screws

- Needles

  - Steel

  - Tungsten

- Tweezers

- Sandpaper stick